Furnish and install a Bryan overflow trap Model __________.  The maximum recommended capacity of the overflow trap shall be _____ PPH.

The overflow trap shall be mounted in the vertical position at the proper level to prevent an overfill condition of excess condensate.

Proper condensate level control insures proper operation of the equipment being controlled and also prevents possible contamination to the service water in a storage compartment.

The overflow trap body shall be constructed of cast iron provided with a heat resistant black paint finish and is provided with a 3/8 inch vent and ¼ inch drain openings.

The interior of the trap shall be furnished with a double-sealed brass valve which is operated by a stainless steel ball float for true reliability and quality operation.

Optional ¾ inch openings are provided on the side of the trap for a gauge glass if required.