Please delete these paragraphs from the standard CLM & K Series Boiler Sample Specification:

The boiler shall be a Bryan Model ________ flexible water tube boiler, with a capacity of ________ BTUH input and ________ BTUH output.  (________ HP)

The boiler shall be constructed and assembled as a completely packaged unit ready for field connections to the water supply, return connection, electrical power supply, natural (propane) gas supply, relief valve discharge, building management controls and flue-gas vent.

The water boiler shall be manufactured in strict accordance with the ASME Heating Boiler Code, Section IV, and shall bear the ASME stamp “H” for a maximum working pressure of 160 PSIG  at 250oF temperature.

#### (Also available for higher pressure up to 250 PSIG and temperatures to 300oF per ASME Section I)

And substitute these paragraphs:

The water heater shall be a Bryan Model ________ Indirect Water Heater, with a capacity of ________ BTU input and ________ BTU output and water heating capacity of ________ gallons per hour, with a temperature rise from ________oF to ________oF.

The water heater shall be constructed and assembled as a completely packaged unit ready for field connections to the water supply, return connection, electrical power supply, natural (propane) gas supply, relief valve discharge, building management controls and flue-gas vent.

The water heater shall be manufactured in strict accordance with the ASME Heating Boiler Code, Section IV, and shall bear the ASME stamp for a maximum working pressure of 125 PSIG at 250oF temperature.

The water heater shall be furnished complete with one or more indirect heat exchangers with a maximum water discharge temperature of 180oF   The heat exchanger(s) shall be installed in the upper drum of the boiler, will be capable of absorbing 100% of the total boiler output as specified and rated operation temperatures.  Heat exchanger(s) to be constructed of heavy copper seamless finned tubing, attached to boiler shell by means of a gasket and stud type connection and shall be easily removable and replaceable.

# WATER HEATER TRIM & CONTROLS

The water heater shall be furnished with the following fittings and trim:

- Automatic boiler fill valve

- Expansion tank

- ASME safety relief valve for heat exchanger

- Boiler stop valve